ClockTHREE-Junior_v2

Assembly and User Guide
# C3Jr_v2

VERSION INFORMATION

KIT VERSION	2

SW VERSION	0_6

USER GUIDE VERSION	1_0

IMPORTANT	1

SAFETY: Please read this MANUAL carefully before assembling the kit. It contains important information, Warning, and Cautions that must be followed to ensure safe operation and to maintain the product in a safe condition.	DO NOT REMOVE COVERS DURING OPERATION: To avoid personal injury or death, do not remove equipment covers without first removing the power source connected to the poduct. Do not operate the product without the covers properly installed.
USE PROPER POWER CORD: Use only the power cord and connector appropriate for the voltage and plug configuration in your country.	Do not attempt to operate if protection may be impaired: If the product appears damaged or operates abnormally, protection may be impaired. Do not attempt to operate the equipment under these conditions. Please contact us.
DO NOT OPERATE IN EXPLOSIVE ATMOSPHERES: To avoid explosion, do not operate the equipment in an atmosphere of explosive gas.

Links	2

www.wyolum.com

http://timewitharduino.blogspot.com/

http://code.google.com/p/clockthree/

http://arduino.cc/

http://www.sparkfun.com/products/9766

Introduction	3

We are so excited for you to build this kit ! The ClockTHREE_Junior is a simpler, smaller version of our ClockTHREE RGB word clock. This is a very easy to build project, which you can likely complete over a weekend, and requires only basic electronics skills. The completed ClockTHREE_Junior, version 2 - a.k.a C3Jr_v2 - will make a fine addition to your home or office and will surely attract a lot of conversation. The C3Jr_v2 shows time using a set of words. A group of LED's located behind the face plate light up individual words to indicate time, such as “IT'S TEN MINUTES PAST FIVE”.

It features mono-color LEDs instead of RGB full color. The LED matrix is smaller at 16 columns and 8 rows, giving a total of 128 addressable LEDs. Other than that, it is similar to the C3 in terms of build instructions. The SW code is also almost the same as that for C3. On the hardware side, we use a 8 bit row driver, instead of the dual 16 bit drivers used in the C3. It is compatible with the Arduino IDE, and uses an ATMega Micro-controller. The kit is provided with the software already installed on the micro-controller.

This guide covers the procedures for assembling the C3Jr_v2 kit. Please exercise appropriate safety practice while soldering. All parts are through-hole mounted, and there are no surface mounted parts for you to solder or worry about. This is an open-source hardware+software project. For design files, source code, & support, please contact us at << info@wyolum.com >>

Before commencing assembly, please read this manual carefully and acquaint yourself with the build process.

The kit consists of the following :
ELECTRONICS - Main Board (PCB), with set of components
- MECHANICAL - A set of Baffles, Front Face Plate, Rear Plate and fixing hardware
- Wall Wart – 12V DC output, 1A

Bill of Materials	4

Bill of Materials	4

Tips, before you start Assembly	5

- Read through and understand the entire set of instructions before you get started. I know, they always say that, but heed the advice this time. It could save you hours of rework and much consternation. We've captured all of the mistakes and blunders made in creating and building the prototypes and tried to foresee problems you may have.
- Take your time. Enjoy the build process and take a break when you feel fatigued. You will have this clock for years to come (and hand it down to your grandchildren!) so there are no worries if it takes you an extra day or week to build it.
- Leave the paper on the front cover and front frame until final assembly. This protects the parts from scratching and smudging.
- Soldering:
  - We assume that this is NOT your first soldering project. If it is, we'd suggest getting a cheap learn-to-solder kit to get started. If this is your first project in a while, here is a quick refresher on soldering. The main thing is to double and triple check that the part is in the correct place with the correct orientation (if applicable). While de-soldering is possible, it is troublesome and time consuming and risky. Make it a goal that you will not have to de-solder in the course of making this clock.
  - After each step, evaluate the solder joints from the front and back of the board. On the back, the solder should be shiny and make a volcano shape, as opposed to a dome shape. On the front, you should see that the solder came all the way trough the board. If it doesn't look good, try re-heating the joint until the plated-through-hole sucks up the solder.
  - Check that the solder does not cause a short to neighboring parts.
  - If you do make a mistake, don't panic. Use a solder sucker to remove the solder and pull the piece gingerly while applying heat. If you damage a trace in the process of de-soldering, send a picture of the damaged area and we will help you make the most of the situation. It may be possible to "blue wire" around the damage.

Resistors	6

RESISTORS / Start by soldering the resistors. The polarity (orientation) does not matter. / PARTS / R1 to R16 : 100 Ohm [brown-black-brown] / R17, R18, R19, R22, R23, R31, R36, R37, R38 : 10k [brown-black-orange] / R20, R21 : 4k7 [yellow-violet-red] / R24, R25, R26 : 1k [brown-black-red] / R30 : 100 Ohm / R32 : LDR (light dependent resistor, may be supported in future release) / R33, R35 : 680 Ohm [blue-grey-brown] / NOTE / R26 : only if DBG LED is used. / R31: only if R32 [LDR] is used. / R36, R37, R38 : only if DS3231 (SMD) is mounted on-board. Not needed if using Chronodot or I2SD.

IC Sockets	6

IC SOCKETS / The sockets are polarized - so make sure to align them correctly with the legend marking on the board. (If you happen to solder one of these in backwards, don't fret, just be sure to plug the IC as indicated on the board). / PARTS / U3 : 28 pin socket, 0.3" width - for ATMega processor / U4 : 24 pin socket, 0.6" width - for Column Driver 74HC154 / U5 : 16 pin socket, 0.3" width - for row driver STP8DP05

Capacitors	6

CAPACITORS / There is one polarized capacitor (C8), and all the others are non-polarized. / PARTS / C3, C6, C9, C10 : 100nF decoupling/filtering capacitors / C8 : 100uF Electrolytic capacitor (polarized) / NOTES / C7 : Reset Capacitor, Not required / C11, C12 : Only required if X1 is a Crystal. Not required if X1 is a 3 pin resonator.

Transistors	6

TRANSISTORS / With transistors, orientation matters. The silk screen indicates the correct orientation. We find that using the middle hole is easier than using the offset hole. / PARTS / Q1-Q16 : 2N5401 [near 100 Ohm resistors] / Q17 : 2N5401 [near Speaker]

Other Parts	6

OTHER PARTS / Finish off by adding in all the other remaining pasts. / PARTS / J1 (or J2 or J3) : The Mini-USB type Power Input socket. Or use the alternative USB-B (J2) or Barrel Socket (J3). / K1, K2 : 3 pin male header pins for Power Select (Wall Wart or USB) and LED ARRAY (Enable or Disable). Both of these also require a shorting link. / P7 : 6 pin, right angle, male header pins for FTDI connector / SP1 : Speaker / Buzzer / SW1, SW2, SW3, SW4, SW5 : right angle push button switches (top access) / OR / SW12, SW22, SW32, SW42, SW52 : straight push button switches (rear access) / X1 : 16MHz resonator (3 pins, not polarized) / R34 : 5k Thumb wheel Dimming Potentiometer (Pot). The Dimming potentiometer allows manual control of the brightness of the LED array. There are a lot of solder pads for this component, to allow various different types of potentiometers to be used. Whichever pot you use, try to make the control accessible from the top of the board.

Optional Parts	6

OPTIONAL & UN-USED PARTS / The board includes several parts that are either optional, planned for future use, or just included in case they're needed. / PARTS / U6 : DS3231 RTC IC. This is an SMD chip that is mounted on the solder side of the board. It may be pre-installed in some cases. If you are planning to use either the I2SD or the ChronoDot, U6 is not required. / BT1 : CR2036 Battery socket and coin Battery. Used only if U6 is installed on-board. / CD1, CD2 CD3 : 4 pin female header sockets, used if you plan to install either the I2SD or the ChronoDot. / D258 + R25 : DBG LED and Resistor – this one is optional, based on personal preference. Some like it installed, some don't. / D260 + R26 : PWR LED and Resistor - this one is also optional, based on personal preference. Some like it installed, some don't. / P1 : 8 way male header to allow fixing the 7 segment, 4 digit LED display from Sparkfun (see Links). / P12 : VOUT – this is an optional 3 way header providing the 5V board supply. / P13 : ISP – For programming the processor. / P41, P42 : C3SB Connectors – Marked as STACK-L and STACK-R, we call this the C3SB (ClockTHREE serial Bus). Allows us to cascade several C3Jr boards).

LED Array	6

LED ARRAY / Install the rest of the LED's for the array. The short lead (Cathode) of the LED always goes toward the label. / This can go very smoothly and quickly. We've found the fastest way to install the field of LEDs is in two steps : even numbered rows and odd numbered rows. This allows ample space for the soldering iron and gets the job done in short order. / PARTS / D1 to D128 : 5mm White LED's